## Slide 1: Number system Conversion
Lecture-4

## Slide 2: The decimal system
The decimal system is the most widely used number system
The decimal system is base 10 (ten symbols, 0-9, are used to represent a number) and similarly, binary is base 2, octal is base 8 and hexadecimal is base 16.
computers only understand binary. Binary, octal and hexadecimal number systems are closely related, and we may require to convert decimal into these systems.
The decimal system is base 10 (ten symbols, 0-9, are used to represent a number) and similarly, binary is base 2, octal is base 8 and hexadecimal is base 16.

## Slide 3: Number System & Description
Binary Number System
Base 2. Digits used: 0, 1
Octal Number System
Base 8. Digits used: 0 to 7
Hexa Decimal Number System
Base 16. Digits used: 0 to 9, Letters used: A- F

## Slide 4: Number System Conversion
Binary to Decimal Number System
Decimal to Binary Number System
Octal to Binary Number System
Binary to Octal Number System
Binary to Hexadecimal Number System
Hexadecimal to Binary Number System

## Slide 5: The general representation of number systems are;
Decimal Number – Base 10 – N10
Binary Number – Base 2 – N2
Octal Number – Base 8 – N8
Hexadecimal Number – Base 16 – N16

## Slide 6: Number System Conversion Table
Binary Numbers | Octal Numbers | Decimal Numbers | Hexadecimal Numbers
0000 | 0 | 0 | 0
0001 | 1 | 1 | 1
0010 | 2 | 2 | 2
0011 | 3 | 3 | 3
0100 | 4 | 4 | 4
0101 | 5 | 5 | 5
0110 | 6 | 6 | 6
0111 | 7 | 7 | 7
1000 | 10 | 8 | 8
1001 | 11 | 9 | 9
1010 | 12 | 10 | A
1011 | 13 | 11 | B
1100 | 14 | 12 | C
1101 | 15 | 13 | D
1110 | 16 | 14 | E
1111 | 17 | 15 | F

## Slide 7: Decimal to Binary Number:
Example 1. Convert (25)10 Solution: Let us create a table based on this question.
Operation Output Remainder
25 ÷ 2 12 1(MSB)
12 ÷ 2` 6 0
6 ÷ 2 3 0
3 ÷ 2 1 1
1 ÷ 2 0 1(LSB)
Therefore, from the above table, we can write,
(25)10 = (11001)2 to binary number.

## Slide 8: Decimal to Octal Number:
Example 2: Convert 12810 to octal number.
Solution: Let us represent the conversion in tabular form.
Operation Output Remainder
128÷8 16 0(MSB)
16÷8 2 0
2÷8 0 2(LSB)
Therefore, the equivalent octal number = 2008

## Slide 9: Decimal to Hexadecimal:
Example 3: Convert 12810 to hex.
Solution: As per the method, we can create a table;
Operation Output Remainder
128÷16 8 0(MSB)
8÷16 0 8(LSB)
Therefore, the equivalent hexadecimal number is 8016
Here MSB stands for a Most significant bit and LSB stands for a least significant bit.

## Slide 10: Other Base System to Decimal Conversion Binary to Decimal:
Example 1. Convert (1101)2 into a decimal number.
Now, multiplying each digit from MSB to LSB with reducing the power of the base number 2.
Now, multiplying each digit from MSB to LSB with reducing the power of the base number 2.
1 × 23 + 1 × 22 + 0 × 21 + 1 × 20
= 8 + 4 + 0 + 1
= 13
Therefore, (1101)2 = (13)10

## Slide 11: Octal to Decimal:
Example 2: Convert 228 to decimal number.
Solution: Given, 228
2 x 81 + 2 x 80
= 16 + 2
= 18
Therefore, 228 = 1810

## Slide 12: Hexadecimal to Decimal:
Example 3: Convert 12116 to decimal number.
Solution: 1 x 162 + 2 x 161 + 1 x 160
= 16 x 16 + 2 x 16 + 1 x 1
= 289
Therefore, 12116 = 28910

## Slide 13: Hexadecimal to Binary Shortcut Method
Hexadecimal Number | Binary
0 | 0000
1 | 0001
2 | 0010
3 | 0011
4 | 0100
5 | 0101
6 | 0110
7 | 0111
8 | 1000
9 | 1001
A | 1010
B | 1011
C | 1100
D | 1101
E | 1110
F | 1111

## Slide 14: Example: Convert (89)16 into a binary number
Solution: From the table, we can get the binary value of 8 and 9, hexadecimal base numbers.
8 = 1000 and 9 = 1001
Therefore, (89)16 = (10001001)2

## Slide 15: Octal to Binary Shortcut Method
Octal Number | Binary
0 | 000
1 | 001
2 | 010
3 | 011
4 | 100
5 | 101
6 | 110
7 | 111

## Slide 16: Example: Convert (214)8 into a binary number.
Solution: From the table, we know,
2 → 010
1 → 001
4 → 100
Therefore,(214)8 = (010001100)2